## Slide 1: Getting Started with RTTY Contesting

## Slide 2: My RTTY History
First license: Tech+ September 1993
Upgraded to General January 14, 1994
First CW QSO January 28, 1994

## Slide 3: My RTTY History
First RTTY QSO 4 Years Later: March, 1998!

## Slide 4: What You Need: Phone

## Slide 5: What You Need: CW

## Slide 6: What You Need: RTTY

## Slide 7: What You Need: RTTY

## Slide 8: Why Do I Like RTTY?
Ability to copy is THE skill that separates average contesters from great on phone and CW.

## Slide 9: Why Do I Like RTTY?
Ability to copy is simply not a factor in RTTY contesting: the decoder does all the work.

## Slide 10: Why Do I Like RTTY?
The RTTY operator can draw other skills, techniques and strategies not applicable to CW/Phone contesting

## Slide 11: Why Do I Like RTTY?
High-performance contesting is enabled for more participants

## Slide 12: Why Do I Like RTTY?
On a good day, I am an average CW contester
On an average day, I am a good RTTY contester
It doesn’t matter what day it is, I am a lousy Phone contester

## Slide 13: Why Do I Like RTTY?
CW contesting is a lean-forward experience:
  Tense
  White-knuckled
  Straining to hear every dot and dash through the static

## Slide 14: Why Do I Like RTTY?
RTTY contesting is a lean-back experience
  Relaxed
  Calm
  I let the computer do the hard work

## Slide 15: Why Do I Like RTTY?
After RTTY Contest
After CW Contest

## Slide 16: Presentation Overview
  Anatomy of a RTTY signal
  Three basic decisions to make as you get started
  Operating demonstration
  Operating essentials
  A look at the future and FT8

## Slide 17: Presentation Overview
Will ignore
  Paddle-generated RTTY
  Using radio memories
  Hardware modems: Hal, Kantronics

## Slide 18: Presentation Overview
RTTY, It’s:
  Like CW in some ways
  Different from CW in other ways

## Slide 19: Anatomy of a RTTY Signal
  Based on work of Emile Baudot, 1870
  Telegrapher
  His goal: create a new communication system with more automation than telegraph and Morse code

## Slide 20: Anatomy of a RTTY Signal
    All RTTY characters are the same length
      CW characters can be from 1 to 6 bits
      CW bits (1’s and 0’s, dit’s and dah’s) are different lengths
    Prior agreement on speed
      CW: the sender picks the speed and recipient must adapt

## Slide 21: Anatomy of a RTTY Signal
  5-bit code:
    C = 01110
    Q = 10111
  5-bit binary code only has 32 combos: 25 = 32

## Slide 22: Anatomy of a RTTY Signal
  Allow each 5-bit code to represent 2 different characters:
    Letters in “letters” character set, 26 characters
    Numbers and punctuation in “figures” character set, 26 characters

## Slide 23: Anatomy of a RTTY Signal
The USTTY or “S-Bell” character set
  Typically the default set used by your software
  A LTRS or FIGS character is transmitted to define whether subsequent characters are interpreted as Letters or Figures
Code | Control Characters | 
00000 | Null | 
00100 | Space | 
01000 | CR | 
00010 | LF | 
11011 | FIGS | 
11111 | LTRS | 
 | Letters | Figures
00011 | A | –
11001 | B | ?
01110 | C | :
01001 | D | $
00001 | E | 3
01101 | F | !
11010 | G | &
10100 | H | #
00110 | I | 8
01011 | J | '
01111 | K | (
10010 | L | )
11100 | M | .
01100 | N | ,
11000 | O | 9
10110 | P | 0
10111 | Q | 1
01010 | R | 4
00101 | S | BELL
10000 | T | 5
00111 | U | 7
11110 | V | ;
10011 | W | 2
11101 | X | /
10101 | Y | 6
10001 | Z | "

## Slide 24: Anatomy of a RTTY Signal
The USTTY or “S-Bell” character set
  Typically the default set used by your software
  A LTRS or FIGS character is transmitted to define whether subsequent characters are interpreted as Letters or Figures

## Slide 25: Anatomy of a RTTY Signal
Send “CQ W9OX”
  CW: 6 Characters plus a pause for the space
  RTTY: 10 Characters
LTRS 11111
C 01110
Q 10111
Space 00100
W 01111
FIGS 11011
9 11000
LTRS 11111
O 11000
X 11101

## Slide 26: Anatomy of a RTTY Signal
  What does it sound like? CW:
  RX is a single audio tone
    Duration of tone (dot/dash) indicates Data 1 or 0
    RX stations pick their preferred audio frequency by selecting their CW offset, commonly from 400 Hz to 800 Hz
    There is a pause between tones or bits
    A longer pause between characters
    A still longer pause between words

## Slide 27: Anatomy of a RTTY Signal
  What does it sound like? RTTY:
  Two audio tones, low & high, identical in length
  The audio frequency of the tone indicates Data 1 or 0
    2125 Hz = Data 1 = “Mark” = low tone
    2295 Hz = Data 0 = “Space” = high tone
    “Shift” = 170 Hz
    One tone or the other is always “on”: 100% duty

## Slide 28: Anatomy of a RTTY Signal
Prior agreement on speed
  Many different rate protocols
  Ham radio contesting uses a bit or tone duration of 22 milliseconds almost exclusively
  This equates to a 45.45 baud or symbol rate (~60 wpm)

## Slide 29: Anatomy of a RTTY Signal
Start and stop bits
  Timing and synchronization
  No info included
  No error correction!
LTRS 11111
C 01110
Q 10111
Space 00100
W 01111
FIGS 11011
9 11000
LTRS 11111
O 11000
X 11101
0
0
0
0
0
0
0
0
0
0
Questions?
11
11
11
11
11
11
11
11
11
11

## Slide 30: Three Important Decisions
  TX: AFSK or FSK?
  Radio to PC interface
  Software

## Slide 31: Then . . .
. . . Versus Now

## Slide 32: Then versus Now

## Slide 33: FSK or AFSK?

## Slide 34: AFSK or FSK?
The ham community is evenly split
Chart: 
| 2010 | 2015
FSK | 68 | 58
AFSK | 32 | 42
Source: rttycontesting.com

## Slide 35: AFSK or FSK?
  FSK: Frequency Shift Keying
    Directly keys transmitter like CW
    A radio-specific feature
    Two control lines from PC serial port to radio aux connector
      Line 1: Continuously grounds PTT input
      Line 2: Toggles FSK/Data/RTTY input

## Slide 36: AFSK or FSK?
  Audio Frequency Shift Keying
    Tones generated in sound card, fed into mic or aux audio input on the radio
    Radio TX is via LSB

## Slide 37: AFSK or FSK?
AFSK
Indirect keying-mic/audio input
Any LSB radio
May be limited by SSB filters
Dial = suppressed carrier freq.
VOX
Sound card
Manage audio levels, compression, Windows sounds
FSK
Direct keying
Radio specific
RTTY RX filters
Dial = Mark freq.
PTT
Com port
No audio level worries

## Slide 38: AFSK or FSK?
FSK or AFSK, which should you use? The answer is:
It won’t make any difference to your QSO partners.

## Slide 39: AFSK or FSK?
See the July/August 2018 NCJ for an unbiased overview of the FSK vs. AFSK choice, and the use of USB-Serial converters, by W0YK.

## Slide 40: Radio to PC Interface

## Slide 41: Radio to PC Interface

## Slide 42: Radio to PC Interface
Radio
Computer
AFSK
Soundcard
audio out
Line In
audio in
Line Out
RX
TX
RTTY decoder/encoder
Radio
Computer
FSK
Soundcard
audio out
FSK & PTT
keying cable
Line In
Serial port
FSK input
RX
TX
RTTY decoder/encoder
PTT
Audio Isolation?

## Slide 43: Radio to PC Interface

## Slide 44: Radio to PC Interface

## Slide 45: Radio to PC Interface
Radio with
Sound Codec
Computer
AFSK & FSK
USB or
Ethernet
RTTY decoder/encoder

## Slide 46: Radio to PC Interface
Chart: 
| RTTY Interface Usage
Std Cables | 325
MicroHam | 305
Other | 290
SignalLink | 180
RigBlaster | 100
Rascal | 30
Navigator | 25
MFJ | 20
Source: rttycontesting.com

## Slide 47: Radio to PC Interface
Commercial interfaces: Typical RTTY Features
  Support for AFSK
  Audio isolation
  Mic/computer audio switching

## Slide 48: Radio to PC Interface
Additional RTTY Features
  Integrated sound card
  Support for FSK
    Direct FSK via legacy serial port
    USB FSK, may require additional software driver

## Slide 49: Radio to PC Interface
Many interfaces include non-RTTY features
  Rig control
  CW interface, possibly a WinKey
Subjective parameters
  Construction features i.e. metal enclosure vs. plastic
  Reviewer comments
  Documentation, support

## Slide 50: Radio to PC Interface
Single Radio AFSK-Capable Interfaces with Audio Isolation |  |  |  |  | 
 | FSK | PC Connect for FSK | Sound Card | List Price | eHam Reviews
Microham Microkeyer II | VCP | USB | Integrated | $429 | 85
Microham Digikeyer II | VCP | USB | Integrated | $329 | 32
WMR RIGblaster Pro | VCP | USB to Serial Cable | PC | $299 | 33
 | Legacy | RS232 |  |  | 
WMR RIGblaster Adv. | VCP1 | USB | Integrated | $200 | 16
WMR RIGblaster Blue | No | N/A | Integrated | $200 | 4
Microham USB III | VCP | USB | Integrated | $199 | 26
Microham USB II | VCP | USB | PC | $159 | 25
WMR RIGblaster P&P | No | N/A | PC | $120 | 42
SignaLink USB | No | N/A | Integrated | $120 | 241
SignaLink SL-1 | No | N/A | PC | $90 | 97
WMR RIGblaster Nomic | No | N/A | PC | $60 | 40
1. Output shared with CW |  |  |  |  | 
Based on August 2015 survey

## Slide 51: Radio to PC Interface
Cables available at an additional cost

## Slide 52: Radio to PC Interface
Should you build your own FSK keying interface?

## Slide 53: Radio to PC Interface
Does your PC have a serial port?

## Slide 54: Radio to PC Interface
Look for the FTDI chipset

## Slide 55: Radio to PC Interface
Must convert RS232 signals to TTL

## Slide 56: Radio to PC Interface
Must convert RS232 signals to TTL

## Slide 57: Radio to PC Interface
Radio connections for FSK are radio specific
Icom 756ProIII

## Slide 58: Radio to PC Interface
Warning: The Com port used for FSK control and the Com port used for rig control MUST be different ports!

## Slide 59: RTTY Software
RTTY Software should:
  Encode your transmissions
  Decode your receive
  Log your QSO’s
  Provide contest-enhancing functionality: packet, rates, multipliers

## Slide 60: RTTY Software
RTTY Software
  N1MM and WriteLog account for nearly 70% of all users
  N1MM share is growing while all other shares are shrinking
Chart: 
| 2015
N1MM | 54
WriteLog | 15
MixW | 7
WinTest | 4
MMTTY | 3
Other | 17
Source: rttycontesting.com

## Slide 61: RTTY Software
MMTTY
  Has a contest interface but probably not your first choice for contest software
  Has an excellent decoder
  Extensively used as a decoder/encoder with N1MM and WriteLog
  Get MMTTY working on a stand alone basis as your first step

## Slide 62: RTTY Software
MMTTY Set up

## Slide 63: RTTY Software
MMTTY Set up

## Slide 64: RTTY Software
MMTTY Set up for
AFSK with VOX

## Slide 65: RTTY Software
MMTTY Set up for
AFSK with VOX

## Slide 66: RTTY Software
MMTTY Set up for
AFSK with VOX
Make sure all audio cables are connected before setting up MMTTY!

## Slide 67: RTTY Software
MMTTY Set up for
FSK
  Determine your Com port number

## Slide 68: RTTY Software
MMTTY Set up for
FSK
  Determine your Com port number

## Slide 69: Getting Started with RTTY
MMTTY Set up for
FSK

## Slide 70: Getting Started with RTTY
MMTTY Set up for
FSK

## Slide 71: Getting Started with RTTY
MMTTY Set up for
FSK Make sure all audio cables are connected before setting up MMTTY!
Sound card transmission
Settings are ignored
when using FSK

## Slide 72: RTTY Software
MMTTY Set up for
USB FSK
Place a copy of extfsk.dll in the MMTTY.exe directory!

## Slide 73: RTTY Software
MMTTY Set up for
USB FSK
Place a copy of extfsk.dll in the MMTTY.exe directory!

## Slide 74: RTTY Software
MMTTY Set up for
USB FSK
This window only appears after all set up windows have been closed

## Slide 75: RTTY Software
MMTTY Set up
Commer-cial interfaces may have their own software and drivers

## Slide 76: RTTY Software
Getting your hardware and software to work together can be challenging.
Don’t be afraid to look for an Elmer
Questions?

## Slide 77: Operating Essentials
Operating Essentials
  Think mouse, not keyboard
  You can operate virtually 100% of a RTTY contest with the mouse, never touching the keyboard

## Slide 78: Operating Essentials

## Slide 79: Operating Essentials

## Slide 80: Operating Essentials

## Slide 81: Operating Essentials
There is no industry standard among radio manufacturers for the FSK shift, up or down
  You might be “upside down” – Mark and Space tones reversed
  Look for a menu setting in your radio to reverse tones

## Slide 82: Operating Essentials
Are you in LSB or USB?
  Regardless of what it says on your radio, AFSK RTTY is done in LSB on TX
  Regardless of what it says on your radio, RTTY RX is always LSB

## Slide 83: Operating Essentials
Unshift On Space
  On by default in MMTTY for TX. LEAVE IT ON!
  On/Off button on the MMTTY control panel for RX. LEAVE IT ON!
  See http://www.dxlabsuite.com/dxlabwiki/RTTYFiguresLettersUSOS or http://www.w7ay.net/site/Applications/cocoaModem/UsersManual/RTTYPage/index.html for more information

## Slide 84: Operating Essentials

## Slide 85: Operating Essentials

## Slide 86: Operating Essentials
“Radiosport is unique in that competitors must cooperate to score points.”
- Ed W0YK

## Slide 87: Operating Essentials
The Challenge: Find the balance between
Short (speed)
Longer with redundancy (fewer fills)

## Slide 88: Operating Essentials
Messages Matter
  Manage redundancy: How and when to repeat exchange elements
    Signal reports: send once, don’t repeat
    Serial numbers: send twice
    Name & QTH: send once or twice

## Slide 89: Operating Essentials
Messages Matter
  Run the default messages for your software for your first few contests
  Then work on optimizing your messages
  Many expert RTTY contesters now recommend the use of CW-like messages
  Adjust redundancy, on the fly if necessary, to match band conditions

## Slide 90: Operating Essentials
Try these:
  Reduce fatigue by lowering headphone volume to a bare minimum
  Eliminate headphones entirely
  Learn your software and try out new features
  Automate yourself – develop muscle memory
  Embrace the Zen of QSO flow

## Slide 91: The Future of RTTY
  FT8 will replace RTTY as the digital mode of choice for DXpeditions
  RTTY will remain a popular HF contest mode into the foreseeable future, but
  FT8 HF contests may emerge

## Slide 92: Getting Started with RTTY Contesting